DHCP and DNS Configuration
Program – 10
DHCP Configuration + Internet Connectivity

Step 1: Configure the DHCP Server as descussed in Program 5 (DHCP Configuration)
- VM1:
  - ens3: 10.0.0.20
  - ens8: 192.168.122.145
- VM2:
  - ens3: 10.0.0.9
- VM3:
  - ens3: 10.0.0.7

Step2: Check VM2 has internet Connection
ping www.google.com
Step3: Go to VM1
- Type following Command
  - sudo -i
  - echo 1 > /proc/sys/net/ipv4/ip_forward
  - sudo iptables -P FORWARD ACCEPT
  - sudo iptables -P INPUT ACCEPT
  - sudo iptables -P OUTPUT ACCEPT
  - sudo iptables -t nat -A POSTROUTING -o ens3 -j MASQUERADE
  - sudo iptables -t nat -A POSTROUTING -o ens8 -j MASQUERADE
Step4: Check VM2 and VM3 for internet Connection
ping www.google.com